## Slide 1
Weekly Reporting
February 20, 2026
Mohansai Sathram
Dr. Yao Hu

## Slide 2
Last Week Summary (Feb 13)
WRF-Hydro v5.4.0 Compiled & Running
• WRF-Hydro = Weather Research & Forecasting Hydrological modeling system by NCAR
• Test case: Croton, New York (Hurricane Irene 2011)
• 6-hour simulation completed successfully (39 output files)
BMI Heat Example: Built & Tested
• BMI = Basic Model Interface (standard API for model coupling, by CSDMS)
• CSDMS = Community Surface Dynamics Modeling System (University of Colorado)
• 49 out of 49 automated tests passed
WRF-Hydro Internals Analyzed
• Identified IRF subroutines (Initialize-Run-Finalize)
• IRF = the pattern of splitting a model into: initialize(), run_one_step(), finalize()
• Mapped 8 key output + 2 input variables to CSDMS Standard Names
• CSDMS Standard Names = universal variable naming convention for model coupling
Documentation & Planning
• Created 8 detailed technical guides covering BMI, CSDMS naming, Babelizer, PyMT
• Created Master Implementation Plan (6 phases, 1,115 lines, full roadmap)
• Studied SCHISM's BMI approach (how SCHISM enables BMI in its source code)
• PyMT = Python Modeling Toolkit (framework that runs coupled models together)

## Slide 3
This Week: Key Topics (Feb 20)
Three main areas of investigation and progress this week:
1
SCHISM's BMI Approach
How SCHISM enables BMI using preprocessor flags directly in its source code
Slides 4-6
2
WRF-Hydro: Why Different?
Why the same approach will not work for WRF-Hydro and what we will do instead
Slides 7-9
3
BMI Template & Heat Model Example
The Fortran BMI template and how the Heat model example demonstrates it
Slides 10-14

## Slide 4
Background: What is BMI?
BMI = Basic Model Interface — A standardized set of functions that any model must implement to be coupled with other models
BMI in Plain Terms
• BMI (Basic Model Interface) is a standard API published by CSDMS (University of Colorado Boulder)
• It defines 41 functions every model must have, such as: initialize, update, finalize, get_value
• Purpose: allow any two models to exchange data without knowing each other's internal code
• Think of it like a universal adapter: any model that implements BMI can plug into any other
• Written in Fortran, C, C++, or Python — each language has its own BMI specification library
• The model's internal code stays untouched; BMI is a wrapper layer on top of it
The 41 BMI Functions (6 Categories)
Category | Count | Key Functions
Control | 4 | initialize, update, finalize
Model Info | 5 | component_name, var_names
Variable Info | 6 | var_type, var_units, var_grid
Time | 5 | current_time, time_step
Get/Set Data | 6 | get_value, set_value
Grid Info | 17 | grid_type, grid_shape, x/y
Every function returns a status code: 0 = BMI_SUCCESS, 1 = BMI_FAILURE Output is always through function parameters, not return values.

## Slide 5
SCHISM's BMI Approach: Inline Preprocessor Flags
SCHISM = Semi-implicit Cross-scale Hydroscience Integrated System Model (ocean/coastal circulation model)
Key Finding: SCHISM does NOT have a separate BMI wrapper file. Instead, it enables BMI by adding conditional code blocks (#ifdef USE_NWM_BMI) directly inside its own source files.
How It Works
• #ifdef = "if defined" — a Fortran/C preprocessor directive that includes or excludes code at compile time (before the code is even compiled)
• USE_NWM_BMI = a flag name (NWM stands for National Water Model, NOAA's operational hydrological model that uses WRF-Hydro)
• When flag is OFF: code inside #ifdef is skipped entirely — SCHISM runs as standalone model
• When flag is ON: extra coupling code activates, allowing SCHISM to receive/send data via BMI
Files with #ifdef USE_NWM_BMI
Source File | Blocks | Purpose
schism_init.F90 | 1 | Validates source/sink settings
schism_step.F90 | 2 | Receives/sends coupling data
misc_subs.F90 | 2 | Adjusts boundary conditions
Total | 5 | Only 5 small code blocks!
Example from schism_init.F90:
#ifdef USE_NWM_BMI
if(if_source==0) then
call parallel_abort('needs if_source>0')
endif
#endif

## Slide 6
Why This Approach Works for SCHISM
SCHISM's architecture is simple enough for inline preprocessor flags to be manageable
Simple Call Structure
SCHISM's main program calls just 3
functions in sequence:
1. schism_init()
2. schism_step() [in a loop]
3. schism_finalize()
This is already the Initialize-Run-
Finalize (IRF) pattern that BMI needs.
No restructuring was required.
Single Grid Type
SCHISM uses ONE grid throughout:
an unstructured triangular mesh
for the entire ocean domain.
Every BMI grid function (get_grid_type,
get_grid_size, etc.) has exactly
one answer — no branching needed.
This keeps the #ifdef blocks
very small and simple.
Shallow Nesting Depth
The driver (schism_driver.F90) is
only 180 lines, 3 levels deep:
main -> schism_step -> physics
#ifdef blocks at level 2 are easy
to read and maintain.
Total files modified: only 3
Total #ifdef blocks: only 5
Coupling Hooks Only
SCHISM's #ifdef blocks are NOT a
full 41-function BMI implementation.
They only add data exchange hooks:
- Receive river discharge input
- Send water elevation output
This is much simpler than a
complete BMI wrapper — just
a few lines per #ifdef block.

## Slide 7
WRF-Hydro: Can We Use the Same Approach?
WRF-Hydro = Weather Research and Forecasting model - Hydrological extension (by NCAR = National Center for Atmospheric Research)
Answer: No. WRF-Hydro's architecture is fundamentally more complex than SCHISM's. Inline #ifdef flags would require modifying 10+ source files and create unmaintainable code.
Side-by-Side Comparison:
Aspect | SCHISM | WRF-Hydro
Call stack depth | 3 levels (simple) | 5 levels (deeply nested)
Main driver size | 180 lines | 2,869 lines
Number of grids | 1 (triangular mesh) | 3 (1km + 250m + channel network)
Source files | ~50 files | 235 files
Time loop structure | Already init/step/finalize | Integrated loop, 5 physics phases
Physics phases per step | 1 ocean step | 5 sequential phases with dependencies
Key Difference: SCHISM already had init/step/finalize separation. WRF-Hydro does not — its time loop mixes initialization, forcing, land surface, routing, and output into one large function.

## Slide 8
WRF-Hydro: Complex Internal Architecture
Each timestep runs 5 sequential physics phases, and the model uses 3 different computational grids simultaneously
5 Physics Phases Per Timestep
Phase 1: Read Forcing Data
Reads atmospheric inputs — rainfall, temperature, wind, humidity, radiation from input files
↓
Phase 2: NoahMP Land Surface
Computes soil moisture, evapotranspiration, snow processes, vegetation dynamics on 1 km grid (NoahMP = Noah Multi-Physics land surface model)
↓
Phase 3: Groundwater
Water table coupling between soil column and aquifer using WTABLE function
↓
Phase 4: Hydrologic Routing
Subsurface flow + overland flow on 250 m grid, then channel routing through river network (this is HYDRO_exe() — 5 levels deep!)
↓
Phase 5: Write Output
Saves results to NetCDF files: streamflow, soil moisture, surface water depth
3 Simultaneous Grids
Grid 0: LSM Grid (1 km)
Uniform rectilinear grid
Variables: soil moisture, snow depth,
evapotranspiration, air temperature
Used by: NoahMP land surface model
Grid 1: Routing Grid (250 m)
Uniform rectilinear grid (4x finer)
Variables: surface water depth,
subsurface flow, overland flow
Used by: terrain routing engine
Grid 2: Channel Network
Unstructured/vector (river reaches)
Variables: streamflow (discharge),
channel coordinates
Used by: Muskingum-Cunge routing

## Slide 9
Our Solution: A Separate Non-Invasive BMI Wrapper
We will write bmi_wrf_hydro.f90 — a single Fortran file that wraps WRF-Hydro without modifying any of its source code
Architecture Overview:
[External Caller: PyMT / Python / Jupyter]
|
bmi_initialize("config.yaml")
bmi_update()
bmi_get_value("streamflow", data)
bmi_finalize()
|
========================================
| bmi_wrf_hydro.f90 (OUR WRAPPER) |
| - 41 BMI functions |
| - Variable name mapping |
| - Grid info lookup table |
========================================
|
Calls WRF-Hydro subroutines:
- HYDRO_ini() / HYDRO_exe()
- land_driver_ini() / _exe()
|
[WRF-Hydro Source Code -- UNTOUCHED]
Why Separate Wrapper Is Better
Aspect | Benefit
Non-invasive | Zero changes to WRF-Hydro
Single file | ~800 lines vs 10+ modified files
Testable | Test wrapper independently
Maintainable | Update WRF-Hydro easily
Full BMI | All 41 functions, 3 grids
Standard | Same pattern as BMI examples
IRF Mapping: initialize() → HYDRO_ini() + land_driver_ini() | update() → land_driver_exe() | finalize() → HYDRO_finish()

## Slide 10
BMI Fortran Template: The Abstract Interface
bmi.f90 — 564 lines that define the contract every BMI-compliant model must fulfill (like an interface specification)
What is bmi.f90?
• An abstract type definition in Fortran 2003 — it declares 53 procedures but provides NO implementation
• Any model that wants BMI must "extend" this type and provide its own implementation of each function
• Published by CSDMS as the bmif_2_0 module (BMI version 2.0, Hutton et al. 2020)
• Installed via conda: bmi-fortran package provides the compiled module and library (libbmif.so)
Key Constants Defined in bmi.f90
! Status codes returned by every BMI function:
integer, parameter :: BMI_SUCCESS = 0
integer, parameter :: BMI_FAILURE = 1
! Maximum string lengths for names:
integer, parameter :: BMI_MAX_COMPONENT_NAME = 2048
integer, parameter :: BMI_MAX_VAR_NAME = 2048
integer, parameter :: BMI_MAX_TYPE_NAME = 2048
integer, parameter :: BMI_MAX_UNITS_NAME = 2048
How Extending Works (Type Inheritance in Fortran):
! bmi.f90 declares (abstract - no code):
type, abstract :: bmi
contains
procedure(bmif_initialize), deferred :: initialize
procedure(bmif_update), deferred :: update
procedure(bmif_finalize), deferred :: finalize
! ... 50 more deferred procedures
end type
! Our wrapper EXTENDS it (provides code):
type, extends(bmi) :: bmi_wrf_hydro
private
! embed WRF-Hydro model state here
contains
procedure :: initialize => wrfhydro_init
procedure :: update => wrfhydro_update
procedure :: finalize => wrfhydro_finalize
! ... implement all 53 procedures
end type

## Slide 11
BMI Heat Model Example: The Physics Model
heat.f90 — A simple 2D heat diffusion model (158 lines). This is the model that gets wrapped by BMI, just like WRF-Hydro will be.
What Does the Heat Model Do?
• Simulates heat spreading across a 2D metal plate
• Top edge is held at a fixed hot temperature (like a boundary condition in hydrology)
• Heat gradually diffuses to neighboring cells using the 2D heat equation (finite difference method)
• Each timestep: new_temp = weighted average of 4 neighboring cells (a 5-point stencil computation)
Model State Variables (stored in heat_model type):
type :: heat_model
integer :: n_x = 0 ! Grid columns (width)
integer :: n_y = 0 ! Grid rows (height)
real :: dt = 0. ! Time step (seconds)
real :: t = 0. ! Current simulation time
real :: t_end = 0. ! End time of simulation
real :: alpha = 0. ! Thermal diffusivity
! Main state variable (2D temperature field):
real, pointer :: temperature(:,:) => null()
end type
3 Model Subroutines
initialize_from_file(model, filename)
Reads 4 values from config file:
alpha (diffusivity), t_end (end time),
n_x (columns), n_y (rows).
Allocates the temperature grid.
Sets initial condition (top row = hot).
advance_in_time(model)
Runs ONE timestep of heat diffusion:
For each interior cell, computes new
temperature as weighted average of its
4 neighbors. Copies result back.
Increments time by dt.
cleanup(model)
Deallocates the temperature arrays.
Frees all memory used by the model.
Called at the end of the simulation.
Hydrology Analogy:
This simple model is to bmi_heat.f90 what WRF-Hydro is to our bmi_wrf_hydro.f90 — the underlying physics engine that the BMI wrapper calls into.

## Slide 12
bmi_heat.f90: The BMI Wrapper (935 Lines)
This file is our blueprint. Every pattern here will be reused when writing bmi_wrf_hydro.f90.
Pattern 1: Type Extension (Embed the Model)
module bmiheatf
use heatf ! Import heat model module
use bmif_2_0 ! Import BMI specification
use, intrinsic :: iso_c_binding ! For pointers
type, extends(bmi) :: bmi_heat
private
type(heat_model) :: model ! Embed model instance
contains
procedure :: initialize => heat_initialize
procedure :: update => heat_update
! ... maps all 53 procedures
end type bmi_heat
Pattern 2: Variable Name Dispatch
! Every variable-info function uses this:
function heat_var_type(self, name, type) ...
select case(name)
case("plate_surface__temperature")
type = "real"
bmi_status = BMI_SUCCESS
case default
type = "-"
bmi_status = BMI_FAILURE ! Unknown var
end select
end function
Pattern 3: get_value (Copy + Flatten to 1D)
! BMI requires all arrays as 1D (flattened):
function heat_get_double(self, name, dest) ...
select case(name)
case("plate_surface__temperature")
! Flatten 2D grid -> 1D array:
dest = reshape(self%model%temperature, &
[self%model%n_y * self%model%n_x])
bmi_status = BMI_SUCCESS
end select
end function
Pattern 4: Control Functions (IRF)
! Initialize: delegate to model's own init
function heat_initialize(self, config_file) ...
call initialize_from_file(self%model, &
config_file)
end function
! Update: advance by exactly ONE timestep
function heat_update(self) ...
call advance_in_time(self%model)
end function

## Slide 13
BMI Driver Program & Data Exchange
bmi_main.f90 (65 lines) — Shows how an external program uses BMI to control the model. The caller owns the time loop, not the model.
BMI Driver: The Caller Controls Everything
program bmi_main
use bmiheatf ! Import the BMI wrapper
type(bmi_heat) :: m ! Create model instance
! Step 1: INITIALIZE (read config, allocate)
status = m%initialize("config.cfg")
! Step 2: QUERY MODEL INFO
status = m%get_component_name(name)
status = m%get_start_time(time)
status = m%get_end_time(end_time)
status = m%get_time_step(dt)
! Step 3: TIME LOOP (caller controls it!)
do while (current_time < end_time)
! Read data OUT of the model:
status = m%get_value( &
"plate_surface__temperature", temp)
print *, "Temperature:", temp(1:5)
! Advance model by one timestep:
status = m%update()
status = m%get_current_time(current_time)
end do
! Step 4: CLEAN UP
status = m%finalize()
end program
How Two Models Exchange Data via BMI
! Future: WRF-Hydro + SCHISM coupling loop
do while (time < end_time)
! Run WRF-Hydro for one timestep
call wrfhydro%update()
! Get river discharge from WRF-Hydro
call wrfhydro%get_value( &
"channel_water__volume_flow_rate", Q)
! Feed discharge into SCHISM
call schism%set_value( &
"channel_water__volume_flow_rate", Q)
! Run SCHISM for one timestep
call schism%update()
end do
Key Observations
• The caller owns the time loop — models do not run themselves; they are stepped externally
• All data access is through get_value/set_value using CSDMS Standard Names (not internal names)
• Config file is the only argument to initialize() — all model settings are read from that file
• Every BMI call returns a status code (0 or 1) — production code should always check these

## Slide 14
Applying the BMI Heat Pattern to WRF-Hydro
Mapping every pattern from bmi_heat.f90 to our bmi_wrf_hydro.f90 — same structure, different model
Pattern-by-Pattern Mapping:
BMI Pattern | Heat Model (Template) | WRF-Hydro (Our Wrapper)
Module name | bmiheatf | bmiwrfhydrof
Embedded model | type(heat_model) :: model | WRF-Hydro state variables (RT_FIELD)
initialize() | initialize_from_file() | HYDRO_ini() + land_driver_ini()
update() | advance_in_time() | land_driver_exe() (all 5 phases)
finalize() | cleanup() | HYDRO_finish() + close files
Grid 0 | 1 uniform_rectilinear (nx * ny) | 1 km LSM grid (ix * jx)
Variables | temperature (1 variable) | streamflow, soil moisture, snow... (8+)
Name mapping | plate_surface__temperature | channel_water__volume_flow_rate, etc.
CSDMS Standard Names Mapping for WRF-Hydro (our initial 8 variables):
Internal Name | CSDMS Standard Name | Units | Grid
QLINK(:,1) | channel_water__volume_flow_rate | m³/s | Channel (#2)
sfcheadrt | land_surface_water__depth | m | Routing (#1)
SOIL_M | soil_water__volume_fraction | dimensionless | LSM (#0)
SNEQV | snowpack__liquid-equivalent_depth | m | LSM (#0)

## Slide 15
Next Steps: Implementation Roadmap
Completed (Phase 1a)
✓ Studied BMI specification (bmi.f90, 41 functions)
✓ Built and tested BMI Heat example (49/49 tests pass)
✓ Compiled WRF-Hydro v5.4.0 successfully
✓ Ran Croton, NY test case (6-hour Hurricane Irene)
✓ Analyzed WRF-Hydro call stack and IRF subroutines
✓ Studied SCHISM's BMI approach (#ifdef pattern)
✓ Mapped 8 WRF-Hydro variables to CSDMS names
✓ Created Master Implementation Plan (1,115 lines)
✓ Created 8 detailed technical reference documents
Immediate Next (Phase 1b)
▶ Refactor WRF-Hydro time loop into IRF pattern (separate init, one-step, finalize)
▶ Write bmi_wrf_hydro.f90 with all 41 functions
▶ Compile as shared library (libwrfhydro_bmi.so)
▶ Write Fortran test driver to validate BMI output against standalone WRF-Hydro run
Future Phases (2-4)
○ Babelize both models (Fortran → Python plugins)
○ Register as PyMT plugins for coupling framework
○ Write coupling script (WRF-Hydro ↔ SCHISM)
○ Test compound flooding case study

## Slide 16
QLINK: The Key Coupling Variable (Streamflow)
QLINK = the Fortran variable inside WRF-Hydro that stores river discharge (streamflow) at every channel link
CSDMS Standard Name: channel_water__volume_flow_rate | Units: m³/s | Grid: Channel Network
Where QLINK Lives in Source Code
What | Details
Declaration | module_rt_inc.F90 (line 160) Inside RT_FIELD derived type
Data type | REAL, allocatable, DIMENSION(:,:) QLINK(nlinks, 2)
Column 1 | QLINK(:,1) = previous timestep flow
Column 2 | QLINK(:,2) = current timestep flow
Access at runtime | RT_DOMAIN(1)%QLINK(1:nlinks, 2)
How QLINK Flows Through WRF-Hydro
1. Forcing data (rain) enters WRF-Hydro
2. NoahMP computes soil water & runoff
3. Overland routing moves water to channels
4. Muskingum-Cunge routing computes:
QLINK(k,2) = flow at link k (m3/s)
5. QLINK written to CHRTOUT output files
as "streamflow" variable in NetCDF
Files That Compute / Store QLINK
Source File | Role
module_rt_inc.F90 | Declares QLINK in RT_FIELD type
module_channel_routing.F90 | Computes QLINK via routing
module_HYDRO_io.F90 | Writes QLINK to CHRTOUT files
module_HYDRO_drv.F90 | Passes QLINK to output routine

## Slide 17
Coupling: WRF-Hydro QLINK → SCHISM ath3 Array
How river discharge computed by WRF-Hydro enters SCHISM's coastal ocean model as source/sink boundary conditions
Data Flow: WRF-Hydro Streamflow → SCHISM Ocean Boundary
WRF-HYDRO BMI LAYER SCHISM
============ ================== ============
module_channel_routing.F90 bmi_wrf_hydro.f90 schism_step.F90
QLINK(k,2) computed by --> get_value("channel_water ath3(:,1,2,1) receives
Muskingum-Cunge routing __volume_flow_rate", Q) river discharge at
for each river link returns QLINK as 1D array --> source/sink nodes
(via #ifdef USE_NWM_BMI)
Variable: RT_DOMAIN(1)%QLINK CSDMS Standard Name: Variable: ath3(nsources,
Shape: (nlinks, 2) channel_water__volume_flow_rate 1, 2, 1)
Units: m3/s Flatten: QLINK(:,2) -> 1D Units: m3/s
How SCHISM Receives Discharge (ath3 array)
• ath3 = SCHISM's source/sink input array (declared in schism_glbl.F90, line 386)
• ath3(nsources, 1, 1:2, 1) stores flow rates at two time levels (for interpolation)
• When USE_NWM_BMI is ON, SCHISM skips reading ath3 from files — BMI provides it directly
• Location: schism_step.F90 (line 1540) and misc_subs.F90 (line 599) #ifdef blocks
Current Coupling Support Status
Direction | Variable | Status
WRF-Hydro → SCHISM | Discharge (QLINK) | Supported (ath3)
SCHISM → WRF-Hydro | Water Elevation (eta2) | Needs Addition
Both directions | Full 2-way coupling | Phase 4 Goal

## Slide 18
Questions for Discussion
Key decisions needed before proceeding with BMI wrapper implementation
Q1: Which WRF-Hydro Variables for BMI?
• WRF-Hydro has 150+ output variables across 8 output file types (CHRTOUT, LDASOUT, etc.)
• BMI does NOT require exposing all variables — we can start with a priority subset
• Currently proposed: 8 output + 2 input variables (streamflow, soil moisture, snow, precip, etc.)
• Which variables are most important for our coupling use case with SCHISM?
Q2: Does SCHISM BMI Support These?
• SCHISM's #ifdef USE_NWM_BMI currently only supports receiving discharge (via ath3 array)
• It does NOT export water elevation (eta2) back to WRF-Hydro — needed for 2-way coupling
• For 1-way coupling (WRF-Hydro → SCHISM): QLINK (streamflow) is sufficient
• For 2-way: SCHISM needs modifications to export coastal water level as BMI variable
Q3: Start with 1-Way or 2-Way Coupling?
• 1-Way: WRF-Hydro sends streamflow to SCHISM (simpler, SCHISM already supports receiving it)
• 2-Way: Also get coastal water elevation back (requires modifying SCHISM's BMI blocks)
• Recommendation: Start 1-way, add 2-way later
• Which approach should we prioritize?
Q4: CSDMS Standard Names Registration?
• Only ~22% of WRF-Hydro variables have existing CSDMS Standard Names
• ~78% need new names to be proposed and registered with CSDMS
• Should we propose new names now, or use temporary names and register later?
• Registration process: submit to CSDMS wiki for community review

## Slide 19
Thank You
Questions & Discussion
SCHISM
Inline #ifdef works because
of simple architecture:
single grid, shallow nesting,
already has IRF pattern
WRF-Hydro
Needs separate wrapper due
to 5-level nesting, 3 grids,
5 physics phases per step,
235 source files
Our Approach
Write bmi_wrf_hydro.f90:
non-invasive, single file,
following bmi_heat.f90
template patterns
WRF-Hydro BMI Wrapper Project | Mohansai Sathram | February 20, 2026